Ver 018.01

HE-300 Wind Turbine System Manual

Website. www.hi-energy.co.kr

Address. 120, Geomdan-ro, Seo-gu, Incheon, Republic of Korea

Tel. 032-502-1308    Fax. 032-502-1309

Contents

1.        Safety Notes Before Use

1.1.        Mechanical risk elements

1.2.        Electrical risk elements

1.3.        Note in assembling

1.4.        Note in installing

1.5.        Note in operating

2.        Overview of HE-300 Wind Turbine

2.1.        Dimension of HE-300

2.2.        Product Component of HE-300

2.3.        Controller of HE-300 System

3.        Installation and Preparation of Wind Turbine

3.1.        Criteria of deciding the installation place

3.2.        Structure (Pole)

3.3.        Groundwork

4.        HE-300 Hybrid controller manual

4.1.        Comprehensive introduction of products

4.2.        Product Parameter

4.3.        Installation and use

4.4.        Parameters setting instructions

4.5.        Special operations of controllers

4.6.        Quality assurance and after-sales service

5.        Maintenance

6.        A/S Rules

1.      Safety Notes Before Use

HE-300 Wind Turbine is designed by considering the safety for its user. However, the wind turbine has risks structural, mechanical, and electric.

Therefore, to assemble and install wind turbines, priority consideration needs to be given to the safety. In addition, it is important to be aware of the risk electric, mechanical, and rotary.

This manual includes structure, procedure, safety maintenance required to install and maintain HE-300 Wind Turbine.

Before installing HE-300 Wind Turbine, it is necessary to read this manual.

The following symbols must be remembered as the sign of risk elements, safety note and etc. in this manual.

|  | This sign indicates a hazard. Don’t do the activity described along with this sign. Great care is needed. |
| --- | --- |
|  | This sign indicate a great problem and damaged device expected to be caused when operating the device on a unstable condition. Caution is required. |
|  | This symbol indicates the notice to be learned certainly during the process. . |

1.1. Mechanical risk elements

- Rotary blades have their inherently mechanical risks. The blades of HE-300 Wind Turbine are made of strong aluminum alloy. HE-300

- The edge is so sharp that great care is needed not to get a cut

- Don’t touch the rotating axis.

- Don’t stop the rotating axis with hands.

- Don’t install HE-300 Wind Turbine on the low place people can reach.

- Don’t let anything touch rotating blades.

1.2.      Electrical risk elements

- HE-300 Wind Turbine is designed with great delicacy in order to avoid electrical risk elements.

- If the wire wrongly connected or smaller than regulatory requirement is used, overload can cause heat or fire on the wire.

- Therefore, it is important to use the wire with proper capacity.

1.3.      Note in assembling

- HE-300 Wind Turbine is released after all the parts are assembled completely.

- External Darrieus Blades and Internal Savonius Blades have only to be assembled.

- This manual indicates the relationship between assembly and wiring in detail.

- Great caution is required for safety all the time during the assembling process.

- Helmet and gloves should be worn for the safety.

1.4.      Note in installing

- The fall of wind turbine installed at the high place can lead to the great risk. Therefore, as much installation as possible is required to be carried on the safe ground.

- It needs to use lift or crane and wear safety gear such as helmet, gloves, safety belt and safety hook when installing.

- In addition, it needs to install wind turbine by deciding to install in a day with no wind. Prepare the tool before construction.

- The installation needs to be carried on the ground as soon as possible.

- Safety gear such as helmet, gloves and safety belt should be worn for the safety.

- After checking the battery is not connected to the facility, the installation needs to be carried.

- The wiring of the generator of HE-300 Wind Turbine needs to be connected to the ground and then the installation needs to be carried with the blades of wind turbine not rotating.

- The rotary axis of wind turbine is required to be placed rightly all the time. Otherwise, it can be difficult to correct distorted blades or level out wind turbine.

- The wind turbine is required to be carried by deciding to install in a day clear and with no wind.

1.5.      Note in operating

- The pole, blades, and electrical wiring of wind turbine need to be checked periodically.

- The blades of wind turbine were designed and produced with hard material but if the blades are hit by external material during the rotation, their damage can be caused.

- Don’t approach the wind turbine during the rotation.

2.       Overview of HE-300 Wind Turbine

HE-300 vertical axis wind turbine is consisting of External Darrieus Blades and Internal Savonius Blades in a S-type as the double structure of drag and lift.

Refer to Picture 1 for the external looks of wind turbine.

[Picture 1] HE-300 Wind Turbine System

| 1 | External blade | 2 | Internal blade | 3 | Generator |
| --- | --- | --- | --- | --- | --- |
| 4 | Damper | 5 | R, S, T Wire |  |  |

2.1.     Dimension of HE-300

- The following Table 1 indicates the technical dimension of HE-300 Wind Turbine.

[Table 1] Dimension of HE-300 Wind Turbine

| General Specification of Part |
| --- |
| Division | Specification of Product |
| Rotor | Diameter | 1300mm | Rated Rotation Speed | 850RPM |
|  | Weight | 20kg | Rotation Speed Range | 0RPM~950RPM |
|  | Amount | 3 units | Material | Aluminum and other alloy |
| Generator | Rated Output | 300WW | Phase | Phase 3 |
|  | Rated Speed | 850RPM | Rated Voltage | 40V |
|  | Pole No. | 16 poles | Rated Current | 12.5A |
|  | Type | Permanent magnet phase 3 alternating current dynamo | Rated Frequency | 50~60Hz |
|  | Speed Range | 0RPM~950RPM | Weight | 10kg |
|  | Excitation Control | Permanent Magnet Type |
| Support Structure Pole | Type | Structural round tube | Height | 6000mm (standard model) -available from 4000mm at minimum |
|  | Material | Steel or SUS |  |  |
|  | Weight | 360kg (standard model) | Connection Type | Bolt (Rock bolt) |
|  | Minimum size(diameter) | Ø139.8mm X 3γ | Protecting Coating | Molten Zinc Plating and other plating |
| Controller | Rated Output | 300W | Output Type | Direct |
|  | Rated Input | Atypical phase 3 40V 12.5A | Rated Output | Single-phase DC 24V 12.5A (12V 25A) |
|  | Input Frequency | 50~60Hz | Output Frequency | 50~60Hz |
|  | Overpower Control Type | Automatically connected control | Overvoltage control type | Automatically connected control |
|  | Storage Battery Voltage | 24V (12V) | System control type | Automatically connected control |
| Brake | Automatic | Connection Control System if over-speeding |
|  | Manual | - |

2.2.      Product Component of HE-300

- Before start to install, all the components to be given needs to be checked through the component list enclosed. If the parts packed in the package are missing or need to be changed, please contact HI-ENERGY KOREA.

[Table 2] Material List of HE-300

| LABEL | Contents | Amount | LABEL | Contents | Amount |
| --- | --- | --- | --- | --- | --- |
| A | External blade | 3EA | B-6 | Damper | 1EA |
| B-1 | Triangle(top) | 1EA | B-7 | 3 Wires of R,S,T | 1EA |
| B-2 | Internal blade | 1SET | C-1 | Bolt and nut of external blade(M10) | 18EA |
| B-3 | Central axis | 1EA | C-2 | Bolt and nut of external blade(M8) | 6EA |
| B-4 | Generator | 1EA | C-3 | French bolt and nut(M8) | 6EA |
| B-5 | Triangle(bottom) | 1EA |  |  |  |

- Table 2 shows the foundation components of wind turbine and it is necessary to use the prescribed components.

2.3.      Controller of HE-300 System

- HE-300 Wind Turbine System basically uses hybrid controller.

- The details can be referred to hybrid controller manual.

3.      Installation and Preparation of Wind Turbine

Please check again if all the materials and tools along with the products are prepared before installing HE-300 Wind Turbine System. Keep it in mind that to check all the information about safety and install safely is more important than to prepare all the tools and equipment necessary for installing the products.

3.1.      Criteria of deciding the installation place

- The system of HE-300 Wind Turbine is designed flexibly in order to satisfy the need and condition of the users. Therefore users can install in all the places users want such as urban area, country, or the roof of the building, or top of the mountain and coast.

- Major core element affecting the operation of all the application programs and the performance of HE-300 Wind Turbine is wind power and therefore it is important to decide the product after deciding the place where wind sources are plentiful.

- Don’t install the system of HQ-300 Wind Turbine in a place where anyone can approach the rotary blades.

- Don’t install the system in a place surrounded by obstacles such as trees and power line.

- Don’t install the system in a place which is hard to control the wind turbine.  HE-300.

- The respects of the limitation or regulation are subject to the local regulation of the place where the relevant product is installed.

- There is a need to make the system put to earth to prevent the lightning toward HE-300 Wind Turbine.

3.2.      Structure (Pole)

- The standard height of Wind Turbine Structure is 6 meters and the general specification is as below.

[Picture 2] Specification Drawing of the Structure

(The details are referred to the floor plan)

- Whether to install it on the ground or whether to install it on the rooftop or roof needs to be considered and whether to bear the weight of HE-300 needs to be considered first.

- The structure designed by HI-ENGERGE KOREA doesn’t need to be purchased in HI-ENERGE KOREA and it is possible to produce and use in the same way of the floor plan provided by local company.

- The structure of Picture 2 is designed by considering the structure as foundation model of HE-300 Wind Turbine system. Therefore, this design is applied as standard structure for HE-300 Wind Turbine System.

- If the system of HE-300 Wind Turbine is to be installed on the roof or rooftop of the building, the structure of the building needs to be checked and it needs to check if the structure bears the shock from the entire weight of wind turbine, gust, wind or earthquake.

- The surroundings need to be checked cautiously when deciding the length of the structure. Be careful not to reach the articles of the surrounding with strong wind or disaster.

3.3.      Groundwork

- HE-300 uses manufacturing foundation (top 400mm X 400mm, bottom 600mm X 600mm, height 1000mm) and it can use its comparable manufacturing foundations.

용융 앙카볼트 Molten anchor bolt

기초 CON’C Foundation CON’C

[Picture 3] HE-300 Foundation Standard

- If installing the system on the ground, please consult regarding the design and component after checking the quality of the soil.

4.      HE-300 Hybrid controller manual

4.1.      Comprehensive introduction of products

4.1.1.      Basic information

Super-intelligent wind/solar hybrid controller is a new type of special high performance control device for new energy application which is designed on the basis of ultra high performance. It contains many years of application experience (such as waterproof, dustproof, salt spray, wiring error, wind resistance limit control of Wind turbine, energy management etc.)

4.1.2.      Characteristics

- Waterproof

Three defenses for circuit board, hierarchical design, even if small amount water enters, it will not damage the device

- RS232 communication

Standard configuration RS232 communication, it is easy to do the monitoring with the computer software. (RS485, short-range wireless is optional). Using a USB to RS232 members, more convenient to exchange data with a computer (computer with USB interface can be used).

- Safety wire connecting

Terminals are treated with injection molding process, wiring short circuit and cross will not occur, more safety for customers’ operating.

- Automatically alarming of battery reverse

Battery input terminal will not be damaged with continuous reverse, and it has buzzer alarm. Avoid equipment damage and fire caused by wiring errors, and better protect the battery.

- Automatically alarming of Photovoltaic panels reverse

Photovoltaic panels will not be damaged with continuous reverse, and it has buzzer alarm. It will not cause wiring errors especially when work at night. (Note: reverse connection detection in the night needs manually keys intervention)

##### Continuous short-circuit output protection

Discharge output terminal has continuous short -circuit protection, and over current protection. It is recovered after the abnormal excluded. Avoid damage of the controller or fire caused by electrical equipment fault (especially the short circuit).

##### Patented Wind turbines stall current limit control technology

Patented Wind turbines stall current limit control methods, which makes Wind turbines not run over current, avoid the damage of expensive generator caused by heating due to over current.

##### Patented Wind turbines stall current limit control technology

Patented Wind turbines stall current limit control methods, which makes Wind turbines not run over current, avoid the damage of expensive generator caused by heating due to over current.

##### Wind turbines input MPPT generation technology (boost)

Controller can provide automatically Wind turbines input maximum power tracking mode, or the 5 segments match curve input configuration mode (input rev to input current; or output voltage to input current curve), which makes the high efficient generation of the Wind turbines, but with low speed.

##### Support multiple output mode selection

This controller provides optional multiple output modes (light control, time control, light on in the morning, PWM dimming, reverse direction), which can satisfy a variety of applications.

##### Statistics the cumulative generating capacity, remaining power, speed,

##### current, temperature and other data

The controller screen displays not only the current, voltage, power of conventional Wind turbines, PV, battery, and the output terminal; but also the cumulative generating capacity of Wind turbines and PV, the remaining battery power, Wind turbines speed, unloading current, and the temperature of controller.

##### Alarm function when terminals up

When the terminals are up, the controller will alarm, which requires customers to use with the correct install direction, avoid the possibility of damage caused by water comes into the controller when used in the open air or due to bad weather.

4.2.      Product Parameter

| Hybrid Controller |
| --- |
| Battery parameters |
| Applied battery voltage | 24V |
| Battery protect method | Reverse connection protection (do not burn any components, with voice prompt); over voltage protection, under voltage protection (for street light and such kind of load) |
| Voltage at the over voltage protection point | 29.0V±0.2V |
| Voltage at the over voltage recovery point | 27.5V±0.2V |
| Voltage at the under voltage protection point | 21.0V±0.2V |
| Voltage at the under voltage recovery point | 23.0V±0.2V |
| Battery temperature compensation | 5mv/℃/2V (settable) (optional component) |
| Wind turbines input parameters |
| Rated power of applied Wind turbines | 300W/12Vor24V |
| Rated power of the terminal | 30Adc (after rectification) |
| Max. input current of the terminal | 40Adc (after rectification) |
| The default speed of the Wind turbines generation with limited speed | 500 RPM (settable) |
| The default current of the Wind turbines generation with limited current | 30A (settable) |
| Wind turbines protection method | over rev protection, over current protection, induction lightening protection |
| Unloading method | PWM stepless high-frequency soft unloading (built-in) |
| MPPT function | Boost MPPT model ( automatic tracking or 5 segments curve tracking) |
| Input current of MPPT channel | 12A |
| PV |
| Rated input current of applied PV | 550W/12Vor24V |
| Rated input current of terminal | 15A |
| Charging voltage drop | <0.2V |
| PV protection methods | Reverse connection protection (Voice prompt) |
| Unloading method | Open circuit unloading |
| Discharge the output port parameters |
| output | 2 outputs |
| Current of each output | 12A |
| Output protection methods | Over current protection (15A/30sec. 18A/0.4sec.), short-circuit protection (current > 150A) |
| Output control methods | light control, time control, reverse output, PWM output (250HZ, only the 2nd output has it) |
| Other |
| Auxiliary function | Monitor of air temperature inside controller, temperature of unloading parts and Wind turbines MPPT components, and also the monitor of control terminals installed on the inversion (with voice prompt) |
| Display mode | Liquid crystal (LCD) display |
| Communication mode | RS232 (5V electrical level)/RS485 (standard) Short-range wireless (optional) |
| Displayed parameters | Wind turbines input voltage/current/power/generated energy/rev/unloading current PV input voltage/current/power/generated energy Battery voltage/charging current/power/total charging capacity/battery status information output current/power/abnormal information of the 2nd output port |
| Power consumption in standby mode (screen backlight closed) | About 20ma /24V system |
| Operating mode | 3M foil key operation (4 keys) |
| Working temperature / humidity range (environment) | -40~+80℃/20~85%RH (noncondensing) |
| Protection grade | IP41 |
| Controller size (L*W*H) | 175mm*148mm *84mm |
| Net weight | 1.8KG |

4.3.      Installation and use

4.3.1.      Installation attention

- Please read this manual carefully before installation.

- Installation should be operated by professional and technical personnel.

- Before installation and maintenance, be sure the controller is uncharged and in the security state.

- Please install the controller at a dry and ventilated place without dust, and avoid rainwater infiltration and direct sunlight.

- When install the cabinet inside, leave enough space around the controller or radiating through box.

- Keep away from corrosive gases and strong electromagnetic interference.

- Installation area should be convenient for installation, electrical connection and later maintenance.

4.3.2.      Installation steps

- Select the installation area (please read the ‘Installation notice’ carefully).

- Check and clean the installation area, and leave enough space for wiring.

- Prepare the installation tools.

- Fix the controller at the installation place.

- Check and be sure the controller is installed firmly.

4.3.3.      Electrical connection

4.3.3.1.    Description of external connection port

[SOLAR INPUT]---Input terminal of solar panel, pay attention to the wiring polarity

## [ BAT  INPUT ]--- Input terminal of battery, which is applicable to the 24V level battery, pay attention to the wiring polarity

## [ WIND INPUT]--- AC input terminal of the Wind turbines, non-polarity input

## [VO+ O1]--- The 1st output terminal. VO+ connects with load positive;

## O1 connects with load negative

## [VO+ O2]--- The 2nd output terminal. VO+ connects with load positive;

## O2 connects with load negative

## Attention: suggest doing wiring according to below order

1. First connect with output load (VO+ 01or VO+ 02)

2.	Then connect with battery

3.	And then connect with solar panel

4.	At last connect with Wind turbines-driven generator

4.3.3.2.    Wiring attention

## Any incorrect operation during the wiring will cause danger, so the wiring operation must be implemented by professionals.

## Please choose the right size, and good insulation cables for electrical connection.

## Make sure the connectors are tighten during the wiring, no virtual connection.

## Avoid loose of connector caused by the shaking of wires during the movable use.

## < Connecting diagram>

4.4.      Parameters setting instructions

4.4.1.      Key Function

## The controller can cooperate with the system to work properly by setting the appropriate parameters. Accrodingly, the controller can monitor and display the set parameters, or dynamic input and output data; it’s easy for debugging and maintenance. The controller enters into the work standby status ([RUN] words flashing) as soon as it is powered and initialized. The controller displays different information according to the different function types, the specific kind to prevail. There are 4 operation buttons on the panel.

| Button | Function description |
| --- | --- |
|  | Page Up |
|  | Page down |
|  | Escape |
|  | Confirm / Enter |

4.4.2.      LCD screen display

## LCD screen can display the following information.

- Mains electricity supply, displayed when mains electricity exits.

- Wind turbines graph, the graph rotates when the rotate; when brakes, displays brakes box.

- Daytime, night indication symbol. In the daytime displays sun, at night displays moon.

- Communication display symbol, temporarily retained.

- Battery voltage level symbol, 12V displays 12; 24V displays 34; displays 48

- Wireless communication display, displays the symbol when has wireless module, displays dynamic symbol during communication.

- The No.1 output status display, when close the output, the symbol not light, otherwise, the symbol light. When short circuit, short circuit symbol displays; when has morning lighting function, and in the state of waiting for morning lighting, light symbol flashing indicates waiting.

- The No.2 output status display, when close the output, the symbol not light, otherwise, the symbol light. When short circuit, short circuit or over loading and such abnormalities, abnormal symbol displays; when has morning lighting function, and in the state of waiting for morning lighting, light symbol flashing indicates waiting (for normal output). If used LED driver module output, then LED symbol displays.

- Solar MPPT symbol, displays when has solar MPPT components, the symbol flashing when the MPPT works.

- Wind turbines MPPT symbol, displays when has Wind turbines MPPT components, the symbol flashing when the MPPT works.

- PV parameter symbol.

Wind turbines parameter symbol.

Battery parameter symbol.

LED drive output parameter symbol.

No.1 output parameter symbol.

No.2 output parameter symbol.

Temperature symbol.

Rev symbol.

- Digital display parameter / status symbol.

- Parameter setting symbol.

- Parameter unit.

- No. 1/2 output/ close status display symbol, displays when has output module, ON corresponding to output open status, OFF to the close status.

- Battery status symbol, displays the rest battery power, after over voltage, displays the over voltage symbol.

- Data checking symbol.

4.4.3.      Browsing of input and output parameters

In the standby screen, press the [ENTER] button, the screen displays the word "WATCH", and press [ENTER] again, first displays the words "PV", which means can check the PV input parameters, in this state, press the page up or down buttons, can switch to other dynamic parameters, corresponding to "PV", "WIND ", " BAT", "OUT1", "OUT2", "TMP", "REV." After selecting the information need to be displayed, press [ENTER], you can enter the parameters class to be displayed currently, each parameter class following several subproject parameters, they can be displayed through up / down buttons. Any time after shows subprojects parameter class, press the [ENTER] can skip to the next parameter class. Any time press [ESC] can exit the parameter display step by step until you return to the standby screen.

For example (in the standby screen)

Standby screen           press [ENTER]            press [ENTER]            press [ENTER]

Below shows all the displayed parameters:

PV------ PV input parameters

S-U--------Solar input voltage (1 decimal point)	Unit: V

S-I---------Solar input current (1 decimal point)  	Unit: A

S-P --------- Solar input power (no decimal point)	Unit: W

S-d ---------Solar input generated energy (no decimal point)	Unit: Kwh

E-U--------Analog voltage of external photosensitive resistor (1 decimal point)	 Unit: V (Use external photosensitive resistor to do day/night checking instead of PV panel)

WIND ----- Wind turbines input parameters

n-U → Wind turbines input voltage (DC voltage after rectification)

(1 decimal point)                                              Unit: V

n-I → Wind turbines input current (DC voltage after rectification)

(1 decimal point)                                              Unit: A

n-P → Wind turbines input power (DC voltage after rectification)

(1 decimal point)                                              Unit: W

n-d → Wind turbines input generated energy (DC generated energy

after rectification) (no decimal point)                     Unit: kwh

n-F → Wind turbines input unloading current (DC) (1 decimal point)	 Unit: A

n-C → Current of Wind turbines charging to battery (1 decimal point)	                                                                       Unit: A

BAT → Battery charging parameters

b-U → Battery voltage (1 decimal point)	                    Unit: V

b-I → Total charging current to battery (1 decimal point)      Unit: A

b-P → Total charging power to battery (no decimal point)     Unit: W   b-d → Total charging capacity to battery (no decimal point)	Unit: Kwh

OUT1 → The 1st output parameters

O1I → The 1st output current (1 decimal point)	          Unit: A

O1P → The 1st output power (no decimal point)		Unit: W

O1T → The 1st output time (no decimal point)	          Unit: Min

OUT2 → The 2nd output parameters

O2I  → The 2nd output current (1 decimal point)                  Unit: A

O2P → The 2nd output power (no decimal point)                  Unit: W

O2T → The 2nd output time (no decimal point)                    Unit: Min

TMP  → Controller internal temperature display

TNP → Controller internal temperature (no decimal point)	Unit: ℃

REV   → Wind turbines rev parameter (RPM)

NSP → Wind turbines rev display (no decimal point)	         Unit: Rpm

4.4.4.      Working parameters setting

The controller can set part of the key parameters through LCD screen. However, some advanced parameters can be set by the extra USB monitoring communication data cable.

In standby state, press the [ENTER], then through the up/down buttons to select [SET], press the [ENTER] again, the controller will be prompted for a password, enter the correct password and press the [ENTER], then you can enter the menu. The default password is: 0000.

## The Key Operating Instructions:

## Enter the menu password input interface, the bit flashes, and every time press Page Down, flashing skip to the next operation bit; every time press Page Up, changes in operating-bit data (+1). After you enter the correct password, you will be prompted to "YES" and then enter into the menu parameter selection area. If wrong, prompts “ERR". Through page up and down to select the current menu. In the current menu, press "ENTER" to enter into the corresponding parameter setting interface immediately, displays the actual setting of parameters. Modify the parameters as above describes, after modifying the parameters, press the "OK" to save the parameter setting immediately, prompt "ERR" if there is an error, no error prompts "YES". Any time, pressing "ESC" to exit. Return to the previous level.

## The controller can display all the setup parameters are as follows.

## 【Add】→【OEY】→【SYS】→【t1O】→【t1F】→【t2O】→【t2F】→【ndS】→【nUt】

## →【bEn】→【nbI】→【CLU】→【SrU】→【nnI】→【nnS】

## 【OEY】 → Enter the password configuration of parameter settings

Description: Through setting of this parameter, every time when you enter the menu to set the parameters, you need to enter the correct password (same with this parameter data) to perform menu operations, default value [000]

【SYS】 → Select 24V system / 12V system / 48V system or automatic                                                       recognition settings

Description: Select 24V system [000], controller works under the configuration of 24V level. Select the 12V system [001], controller works under the configuration of 12V level. Select the 24V systems [002], controller works under the configuration of 48V level Select automatic system [003], controller works under the configuration of automatic voltage recognition. Default: [000]

【T1O】【T1F】 → These two parameters are combined for controlling the output: the 1st output method.

Description:

【T1O】=0	【T1F】=0	range 0-16 hours

-Output in the night: (through LCD screen, only this mode can be set)

The 1st output is light control output mode: that means output after dark; closed after dawn.

【T1O】>0	【T1F】=0	range 0-16 hours

-Output in the night: (through LCD screen, only this mode can be set)

The 1st output is time control output mode: output at night, closed when the set time arrived. If the setting time has not arrived, but already in the daytime, output will be closed.

【T1O】=0	【T1F】>0	range 0-16 hours

-Output in the night and output in the day are all valid

The 1st output maintains continuous output mode: that means maintain a continuous output for 24 hours unless there is abnormality occurs (under voltage, over current, short circuit, etc.)

【T1O】>0	【T1F】>0	range 0-16 hours

Output in the night: (through LCD screen, only this mode can be set)

The 1st output is morning lighting mode output: that means, after dark, output opens; close output when last time reaches to [T10] setting time, and transfer to a waiting state, waiting till to the [T1F] setting time, continue to open the output, until to the morning.

【T2O】【T2F】 → These two parameters are combined for controlling the output: the 2nd output method

Description:

【T2O】=0	【T2F】=0	range 0-16 hours

-Output in the night: (through LCD screen, only this mode can be set)

The 1st output is light control output mode: that means output after dark; closed after dawn.

【T2O】>0	【T2F】=0	range 0-16 hours

-Output in the night: (through LCD screen, only this mode can be set)

The 1st output is time control output mode: output at night, closed when the set time arrived. If the setting time has not arrived, but already in the daytime, output will be closed.

【T2O】=0	【T2F】>0	range 0-16 hours

-Output in the night and output in the day are all valid

The 1st output maintains continuous output mode: that means maintain a continuous output for 24 hours unless there is abnormality occurs (under voltage, over current, short circuit, etc.)

【T2O】>0	【T2F】>0	range 0-16 hours

-Output in the night: (through LCD screen, only this mode can be set)

The 1st output is morning lighting mode output: that means, after dark, output opens; close output when last time reaches to [T20] setting time, and transfer to a waiting state, waiting till to the [T2F] setting time, continue to open the output, until to the morning.

【NDS】 → Pole pair number set of the wind generator, used for measuring the Wind turbines speed

Generally, wind generators are permanent magnet synchronous generator, how many magnets inside; half is the number of pole pairs, for example, if there are 8 magnets, the number of pole pairs is 4.

Range: 2-100	default: 4 pairs

【NUT】 → Sustained braking time parameter set after Wind turbines braking

After the Wind turbines brakes, Wind turbines can be released after the brake time set by this parameter, and continue to generate electricity (except: after Wind turbines brakes, if the brake current is too large, and do not reduce even last for some time, the controller will release the braking action, and recheck brake conditions after a period of time, if OK, re-brake, again and again, to avoid burn generator or controller due to large current, limited current set by [NNI] parameters)

Range: 1-59	default: 20 minutes

【BEN】 → The buzzer sound enabled settings

When this parameter is set to [001], enable buzzer alarm

Following states will cause the buzzer ring.

- A key input

- The battery reversed

- PV panels reversed

- The temperature is too high

- The 1st output is short circuit, over current

- The 2nd output is short circuit, over current

- The controller terminals is upward

【NBI】 → Wind turbines MPPT charging components maximum input current limit setting

1 – In the automatic power tracking mode (only can be set by USB data wire)

This parameter is used to control the input current through the MPPT parts; and on the other hand, control the matching of Wind turbines input impedance, if the value is set too small, the MPPT algorithm is inefficient, but does not pin down the Wind turbines; If it is set too large, the MPPT algorithm is high efficient, but may be drag Wind turbines in low wind speed. So they need a reasonable set according to Wind turbines power curve.

For example, in the low wind speed (such as 4.5 m/s), the Wind turbines can output the maximum power under 2A current, and will not cause the stall run of Wind turbines (pin down the Wind turbines, speed can’t be improved), then this parameter should be set to 2A, that is [NBI] = 20, there is a decimal point: 2.0A

(Range 0-50 or 0-5A current. Specific depend on the maximum power configuration of MPPT module.)

2 - 5In the 5 segments matching mode (only can be set by USB data wire)

Through USB data wire to set the 5 points Wind turbines curve of rev-current, or voltage-current, the set current will be limited by the [NBI] parameter. As the controller includes the main charging passage of the Wind turbines, MPPT low voltage charging passage, so this parameter restricts the maximum input current of MPPT low voltage charging, can avoid over current running of MPPT low voltage boost charging passage.

After set running in the curve matching, the controller will extract the input current from the Wind turbines to charge the battery according to this charging curve. Generally, recommend the experienced customers use this mode to match with the Wind turbines, to have the best generating effect.

【SrU】 → Starting voltage setting of MPPT charging input carried out by Wind turbines

input voltage of Wind turbines is over this setting parameter, MPPT stat charging, the controller does the maximum power tracking to Wind turbines input automatically. (o 5 segments curve matching)

【CLU】 → Input voltage setting corresponding to close the Wind turbines charging

When the input voltage of Wind turbines is lower than setting parameter, close the charging to MPPT, can avoid stopping of Wind turbines under a very low speed.

【NNI】 → Wind turbines maximum input current setting

Wind turbines input current for generating exceeds the current set by this parameter, will cause a controlled braking action, combining [NUT] parameter, and finish the brake control.

Range 0-500, which is 0-50.0A	default 18.0A

【NNS】 → Wind turbines maximum rev limit setting

When the Wind turbines speed reaches the speed set by this parameter, the controller controls the speed within this parameter setting value through unloading automatically, stable the maximum speed, if the Wind turbines speed is too large, exceeds the automatic steady speed range, continue for some time, will start braking, braking time decided by [NUT].

Range 0-3000 rev/min  default 500

【Add】 → Communication code of the controller

Give a code to different device during the multiple communications; every controller code must be different with others, to avoid crosstalk.

Range 2 – 250	default 6

4.5.      Special operations of controllers

4.5.1.      Manually unloading operation

In standby mode (the controller displays ‘RUN’, and blinking), long press the [ESC] button for 3 seconds, the Wind turbines will enter into manual brake status immediately, the Wind turbines graphic symbol shows as a frame, and the Wind turbines is framed by it, which means it’s braking now. If now you press [ESC] for 3 seconds, the braking action will be released slowly, and the Wind turbines generates again.

4.5.2.      Controller warm reset start

Press page up and down buttons simultaneously for 3 seconds, LCD digital part displays "RST", the controller is reset immediately, reinitialize working. The effect is the same as remove the power and then energized.

Recommend to perform this operation to reset controller after setting all the parameters, or encounter problems.

4.5.3.      Manual testing of PV input reverse (for wiring in the night)

When connect the solar panel in the night, this function is used to detecting whether there is a reverse function (when wiring in the daytime, this function is failure). In standby mode (the controller displays ‘RUN’, and blinking), long press the page up button for 3 seconds, the controller displays ‘-C-’, continuously check if the solar panel is reversed. If reverse is exists, displays ‘Err’, recheck after correcting, if OK, no error information will appear.

4.6.      Quality assurance and after-sales service

One year warranty from the date of the products sold. Within the warranty period, the product failures caused by normal use, our company will provide free repair or replacement. If the warranty period has expired, our company still provides maintenance services, but requires a fee.

The product warranty is only available to the original purchaser, and it is not transferable. Our company reserves the right to change products, product updates without notice. One of the following conditions occurs within the warranty period, our company will not provide free services.

5.      Maintenance

5.1.      Application Range

This procedure applies to the guidance regarding maintenance after takeover.

5.2.      Goal

This procedure is pertaining to the maintenance other than receiving the complaints of customers. And its goal is to check and maintain the status of wind turbine normally or periodically.

5.3.      How to maintain

- Wind Turbine

1) Visual Inspection

| Inspection Contents | Notice |
| --- | --- |
| Whether wind turbine is rotating |  |
| Whether the blades are broken and transformed |  |
| Whether there is serious noise or mechanical sound during rotation |  |

- Controller

1) Visual Inspection

| Inspection Contents | Notice |
| --- | --- |
| Check if the power is normally provided | Check if the lamps on the battery part of the controller turns on DC12 or 24V |
| Check if wind turbine and solar module is charged | Check if the lamp on the controller, wind power and solar power turns on |

5.4.      Follow-up care

- The flaw and defect detected during onsite inspection needs to be reported to the manager of onsite facilities. The internal inspection needs to be conducted according to the above method of maintenance.

- If the facility manager or other staff detects flaw and defect, it needs to report it to relevant company and the staff other than technician should not operate. (But, after the consultation with technicians, the parts to be handled onsite can be processed onsite.)

- The company should accept it within maximum 14 days when receiving complaints from customers. (asking after-sales service) (If it can’t be possible to accept the complaints within 14 days, consult the manager of onsite facility regarding the schedule and progress and process the situation.

5.5.     Product Assurance and Defect Assurance Insurance

- Sales and Installation in Korea

The period of Free and Paid Assurance and Defect Assurance Insurance of the products sold and installed is defined as follows;

| Contents | Assurance Period | Division of Free or Paid |
| --- | --- | --- |
| Durability of the Product | 10 years | Paid after 2 years |
| Product assurance(blades, generator, and main product) | 2 years | Free |
| Products Assurance(inverter, controller, and charger) | 1 year | Free |
| Defect Assurance Insurance | 2 years | Seoul Guarantee Insurance |

6.      A/S Rules

If not disorder, there is an extra charge when calling for service. Therefore, read the manual and provide the consulting through telephone in the case of not able to handle through manual.

6.1.      Repair for free

- In case of disorder of function or performance occurring during the normal use within the period of quality assurance.

- In case of reoccurring disorder on the same part within 2 months after the repair by CS Professional(engineer)

6.2. Repair at a cost

- Product whose warranty period runs out.

- In case of explanation and simple arrangement of manual without overhaul.

- In case of external environment problems such as internet, antenna and wired signal.

- In case of connecting or re-connecting product additionally after initial installation of the purchased products.

- In case of asking additional installation after purchasing the product in the place other than official distributor.

- In case of changing the installation place because of the moved product and moving.

- In case of disorder caused by using product of other company. (including software)

- In case of disorder because of not following the notice of the manual.

- In case of disorder caused by using wrongly the electricity capacity.

- In case of disorder caused by consumables or optional product not designated by our company.

- In case of disorder caused by the repair by the person other than CS professional engineer.

- In case of the disorder or damage caused by external shock or falling.

- In case of the disorder caused by natural disaster including lightening, fire, earthquake and tsunami.

- In case of the consumable parts such as battery and lamp coming to an end.

6.3.      Criteria to decide service fare

Service fare               Parts cost           Repair cost               Travel expenditure

(engineering fee)

- Service fee is consisting of the total amount with parts cost, repair cost, and travel expenditure and each fee is decided as follows.

※ The applied standard can be different when the products are purchased overseas.

- Parts cost

- Parts cost, equipment cost and etc. required when parts are changed during the repairs.

- Parts cost includes 10% of VAT

- Repair cost

- Repair cost indicates the engineering fee other than parts cost and it is estimated by considering the required time and difficult level during the paid repair but it is included in travel expenditure.

- Travel expenditure

- Travel expenditure is applied in the case of asking the onsite service and calculated separately for the different region. (In principle, travel expenditure needs to be paid in advance)

| Region | Days/person | Amount | Notice |
| --- | --- | --- | --- |
| Seoul·Gyeonggi | 1 day/ person | 150,000 |  |
| Chungcheon/Ganwon | 1 day/ person | 300,000 |  |
| Jeolla/Gyeongsang | 1 day/ person | 500,000 |  |
| Highlands and islands | 1 day/ person | 800,000 | Not include room charge |

6.4.      Criteria to estimate assurance period

- HI-ENERGY KOREA conducts the assurance for the product as follows according to Consumer Dispute Resolution Criteria by contents announced by Fair Trade Commission.

- Product Warranty Period

- Product Warranty Period mean the time manufacturer or distributor promises to repair free of charge for the defect in quality, performance and function occurring in a normal state to customer.

- Warranty Period is estimated based on the date of release and the date is according to the Warranty Certificate (including purchase receipt). However, if there is no warranty, warranty condition will be decided in accordance with the warranty certificate issued by the company at the time of manufacturing the relevant product. The warranty period will be estimated by considering 3 months (reflecting circulation period) in the date of production.

- In case of the purchase of used items (item purchased in non-designated distributor or fake), the above warranty period is not applied and in the case that the repair is not available, our company will not be responsible for the damage compensation.

- The warranty for the product delivered with separate contract with our company will be based on the relevant contract.

6.5.      Warranty Period by Items

- Warranty period of the parts

- Warranty period of the parts means the warranty for each part consisting of the product and the period is as follows;

| Items | Warranty for free | Details | Notice |
| --- | --- | --- | --- |
| Wind Turbine | 2 years | Main body of wind turbine |  |
| Electric and electronic parts | 1 years | Inverter, controller, timer, converter, solar panel, LED lamp and others |  |
| Structure | 2 years | Support structure |  |
| Others | - | Follow the warranty period of company |  |

- In case of repairing at a cost and in case that the same disorder occurred during the procedure of using the product normally within 2 months from repair day